## Slide 1
Data access mechanism:
  Geology machine readable options, any of:
    SQL
    WxS (WFS/WCS NOT WMS)
    OPenDAP
    NetCDF
    Or in fact any direct internet data access protocol. Preferably one that can specify use a bounding box to avoid massive data downloads
    ESRI Shapefiles & Mapinfo Tab files
  Geophysics machine readable options:
    GA’s geophys_utils python library provides enough access for now
  Drillhole data access:
    Any SQL with geospatial capabilities
  DTM:
    Sourced from one of a number of online servers (e.g. opentopography.org)

## Slide 2
Data:
  Geology Polygons :
    At least two levels of stratigraphic coding (e.g. formation/group)
    Lithological description that allows us to discriminate between sills, other intrusive, and sedimentary/volcanic formations
    At least one absolute or relative age estimate or max/min estimates for each formation/unit
    Optional:
      Master sorted list of stratigraphic units to resolve relative age ambiguities
  Fault and fold axial trace polylines:
    Faults and fold axial traces can be same file, if field with discriminator is present
    Field with unique identifier for each fault
    Fold axial trace synform/antiform/syncline/anticline information
    Optional:
      if fault dips are available, great!
      if sense of displacement is available, great!
  Structural observation points:
    Field that discriminates between observation types (bedding, cleavage, lineation etc)
    Dip
    Dip direction or strike
  Mineral deposits (optional):
    Commodity

## Slide 3
Data:
Company or survey drillhole data (Optional):
  Standard drillhole data with from/to pairs & survey information
  Stratigraphic data if for immediate
  Database schema!
  Optional:
    Machine readable dictionaries and/or freeform text descriptions of lithology
Sections (Optional):
  Layer with section trace polyline
  Layer with faults and stratigraphic contacts as polylines with:
    Field to discriminate faults and stratigraphic contacts
    Field to label faults and stratigraphic contacts
  Layer with three points defining top-right, bottom-right, top-left in section coordinates (distance along section, depth)